## Slide 1: Binary Numbers
March 25 2018
Art without Engineering is dreaming. Engineering without Art is calculating.
- Steven K. Roberts

## Slide 2: Overview & Introduction
This lesson is designed to introduce you to the Binary (base 2) number system. Binary is used in all modern computer systems and logical operations
You learn how to convert numbers from the Decimal (base 10) to Binary (base 2).
You will also learn how to add and multiply in Binary.

## Slide 3: See Appendix A, for Licensing & Attribution information
by-nc-sa-3.0
https://creativecommons.org/licenses/by-nc-sa/3.0/
https://creativecommons.org/faq/#what-does-some-rights-reserved-mean

## Slide 4: What You Will Know…
Prior Knowledge
  You should have an understanding of how the Base 10 number system works
  How and why we carry when we count from 9 to 10 or 99 to 100
  Understand the concept of the "One's", "Ten's" and "Hundred's" place values.
What You Will Know & Be Able To Do
  You will be able to count in Binary
  How to convert numbers from Binary (base 2) to Decimal (base 10) and from Decimal to Binary
  You will know how to add in Binary
  How to multiply in Binary

## Slide 5: How Will You Be Measured
You will be asked to participate in class discussion, and I will evaluate your understanding based on your answers
You will answer questions in online quizzes and or worksheets and points assigned based on right/wrong answers

## Slide 6: New Words or Concepts…
Binary
Number System
Place Value
Digit
Bits, Bytes, Words

## Slide 7: “Let’s Play A Game”

## Slide 8: I Need A Volunteer…
Pick A Number Between “0” And “64”
  So Not “0” or “64”, But Some Whole Number In Between…
Write It Down
Show It Around… But Don’t Let Me See It
Place it Face Down On Your Table
Now, Tell Me “Yes” Or “No” If Your Number Is On The Next 6 Slides
Ready…

## Slide 9: Is Your Number on this card?
1 | 3 | 5 | 7 | 9 | 11 | 13 | 15
17 | 19 | 21 | 23 | 25 | 27 | 29 | 31
33 | 35 | 37 | 39 | 41 | 43 | 45 | 47
49 | 51 | 53 | 55 | 57 | 59 | 61 | 63

## Slide 10: Is Your Number on this card?
2 | 3 | 6 | 7 | 10 | 11 | 14 | 15
18 | 19 | 22 | 23 | 26 | 27 | 30 | 31
34 | 35 | 38 | 39 | 42 | 43 | 46 | 47
50 | 51 | 54 | 55 | 58 | 59 | 62 | 63

## Slide 11: Is Your Number on this card?
4 | 5 | 6 | 7 | 12 | 13 | 14 | 15
20 | 21 | 22 | 23 | 28 | 29 | 30 | 31
36 | 37 | 38 | 39 | 44 | 45 | 46 | 47
52 | 53 | 54 | 55 | 60 | 61 | 62 | 63

## Slide 12: Is Your Number on this card?
8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
40 | 41 | 42 | 43 | 44 | 45 | 46 | 47
56 | 57 | 58 | 59 | 60 | 61 | 62 | 63

## Slide 13: Is Your Number on this card?
16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
48 | 49 | 50 | 51 | 52 | 53 | 54 | 55
56 | 57 | 58 | 59 | 60 | 61 | 62 | 63

## Slide 14: Is Your Number on this card?
32 | 33 | 34 | 35 | 36 | 37 | 38 | 39
40 | 41 | 42 | 43 | 44 | 45 | 46 | 47
48 | 49 | 50 | 51 | 52 | 53 | 54 | 55
56 | 57 | 58 | 59 | 60 | 61 | 62 | 63

## Slide 15: Your Number IS…….

## Slide 16: Why Do We Count To 10?
Because We Have 10 Fingers…
What If We Had 3 fingers?
How About If We Only Had 1?
Let’s Learn About The Binary (Base 2) Number System,
But First, Lets Review The Decimal (Base 10) Number System
A2

## Slide 17: Base 10 Number System - Place Value
Which Number is bigger?
    39 or 93
3 9 9 3
10 1 10 1
3x10 + 9x1 9x10 + 3x1
30 + 9 90 + 3
____ ____ ____ ____ ____
1000
100
1
10
Place Value
10000
5 6 3 9
1000 100 10 1
A4

## Slide 18: Base 10 Number System - Place Value
11
0 to 9
____ ____
1
10
??
____ ____ ____ ____ ____ ____
1000
100
1
10
Place Value
10000
X 10
Because it’s Base 10
Why?
Only Allowed One Digit Per Place Value
How Do You move from one Place Value to the next?
What Digits are allowed for each Place Value?
(10 Digits)
3
9
A5
\
1

## Slide 19: Figuring Out Other Base Number Systems
Base 16
Base 2
P.V.
x ?
1
P.V.
x ?
65536
1048576
4096
____ ____ ____ ____ ____ ____
Place Value
____ ____ ____ ____ ____ ____ ____ ____
Place Value
256
16 Digits = F,E,D,C,B,A,9,8,7,6,5,4,3,2,1,0
2 Digits = 1,0
16
…
x 16
x 2
A10
??… 128 64 32 16 8 4 2 1
___
256

## Slide 20: Base 2 Number System - Place Value
____ ____ ____ ____ ____ ____ ____ ____
Place Values
You Use The Same Rules As Decimal (Base 10)… Just In Binary (Base 2)
How Do You move from one Place Value to the next?
In Other Words, How Do You Count In Binary
… 128 64 32 16 8 4 2 1
A1

## Slide 21: Counting In Binary
Remember Binary Numbers are made of 0s and 1s
Here Is An Example Of A Binary Number: 101011
  Binary Number can only be made from the Digits 0-1
  There is no 2,3,4,5,6,7,8 or 9 in Binary
Lets Start Counting…
Start with 0
Then count to 1
Then ?? There is not symbol for 2
A1
Place Values
Play

## Slide 22
Binary is as easy as 01, 10, 11
Convert the Following Binary Numbers:
Computer Humor
1x2 + 1x1 = 3
1x8 + 0x4 + 1x2 + 1x1 = 11
1x16 + 0x8 + 1x4 + 0x2 + 1x1 = 21
0011 = ?
1011 = ?
10101 = ?
110011 = ?
1x32 + 1x16 + 0x8 + 0x4 + 1x2 + 1x1 = 51
Place Values
Place Values
____ ____ ____ ____ ____ ____ ____ ____
… 128 64 32 16 8 4 2 1
A7

## Slide 23: Bits and Bytes?
How does a computer count?
It Uses The Binary (Base 2) number system?
Bits, Bytes, Words
You See the Number 3, The Computer Sees 0011
Decimal (Base 10 ) | Binary (Base 2) | Hex (Base 8)
0 | 0000 0000 | 0
1 | 0000 0001 | 1
2 | 0000 0010 | 2
3 | 0000 0011 | 3
4 | 0000 0100 | 4
5 | 0000 0101 | 5
6 | 0000 0110 | 6
7 | 0000 0111 | 7
8 | 0000 1000 | 8
9 | 0000 1001 | 9
10 | 0000 1010 | A
11 | 0000 1011 | B
12 | 0000 1100 | C
13 | 0000 1101 | D
14 | 0000 1110 | E
15 | 0000 1111 | F
16 | 0001 0000 | 10
Some Computer Architectures
A WORD = 4 BYTES = 64 Bits
0000 0000 0010 1001
BIT
BYTE = 8 Bits
WORD = 2 BYTES = 32 Bits
4110 = 0010 1001
25410 = 1111 1110
25510 = 1111 1111
25610 = 0001 0000 0000
1 BYTE

## Slide 24: All Six Cards
Decimal (Base 10 ) | Binary (Base 2)
0 | 0000 0000
1 | 0000 0001
2 | 0000 0010
3 | 0000 0011
4 | 0000 0100
5 | 0000 0101
6 | 0000 0110
7 | 0000 0111
8 | 0000 1000
9 | 0000 1001
10 | 0000 1010
11 | 0000 1011
12 | 0000 1100
13 | 0000 1101
14 | 0000 1110
15 | 0000 1111
16 | 0001 0000

## Slide 25: All Six Cards
128 = 27
0 0 0 0 0 1 1 1
= 7
64 = 26
4 = 22
2 = 21
1 = 20
32 = 25
16 = 24
8 = 23

## Slide 26: All Six Cards
128 = 27
0 0 0 0 1 1 0 1
= 13
64 = 26
4 = 22
2 = 21
1 = 20
32 = 25
16 = 24
8 = 23

## Slide 27: All Six Cards
128 = 27
0 0 0 1 0 0 0 0
= 16
64 = 26
4 = 22
2 = 21
1 = 20
32 = 25
16 = 24
8 = 23

## Slide 28: All Six Cards
128 = 27
0 0 0 1 1 0 1 1
= 27
64 = 26
4 = 22
2 = 21
1 = 20
32 = 25
16 = 24
8 = 23

## Slide 29: All Six Cards
128 = 27
0 0 1 0 1 0 0 1
= 41
64 = 26
4 = 22
2 = 21
1 = 20
32 = 25
16 = 24
8 = 23

## Slide 30: Ready For a Quiz?
Web based Google Quiz
  Decimal 2 Binary Quiz #1
  Decimal 2 Binary Quiz #2
  Binary 2 Decimal Quiz #3
  Binary 2 Decimal Quiz #4
Worksheet Hand Out

## Slide 31: Adding Binary Numbers
https://www.quickanddirtytips.com/education/math/how-to-add-binary-numbers?page=1
110
+ 101
1011
Since 0 + 1 =1
Since 1 + 1 = 10
Since 1 + 0 = 1
Rule 1  0 + 0 = 0
Rule 2  0 + 1 = 1
Rule 3  1 + 0 = 1
Rule 4  1 + 1 = 10  Surprise!
Just like
decimal
addition
}

## Slide 32: Multiplying Binary Numbers
https://www.quickanddirtytips.com/education/math/how-to-add-binary-numbers?page=1
110
* 101
1 1 0
0 0 0 0
1 1 0 0 0
11110
Rule 1  0 * 0 = 0
Rule 2  0 * 1 = 0
Rule 3  1 * 0 = 0
Rule 4  1 * 1 = 1
Just like
decimal
multiplication
}

## Slide 33: Adding and Multipying in Binary
Adding Binary Numbers
  Adding in binary | Applying mathematical reasoning
Multiplying Binary Numbers
  Multiplying in binary | Applying mathematical reasoning

## Slide 34: Reference Slides

## Slide 35: Resources & Materials
Lecture Slides (PDF)
Student Worksheets (PDF) or Link to Google Quiz
Student “Let’s Play A Game” Handout & Instructions

## Slide 36: Appendix

## Slide 37: Appendix A: License & Attribution
This interpretation is primarily the Intellectual Property of Jim Burnham, Top STEAM Clown, at STEAMClown.org
This presentation and content is distributed under the Creative Commons License CC-by-nc-sa-3.0
My best attempt to properly attribute, or reference any other sources or work I have used are listed in Appendix B

## Slide 38: Appendix B: Attribution for Sources Used
Decimal/Binary Conversion Quiz - http://acc6.its.brooklyn.cuny.edu/~gurwitz/core5/binquiz.html
Online Magic - http://avimagic.com/tricks/number_cards.php
Binary Trick - http://www.mathmaniacs.org/lessons/01-binary/Magic_Trick/
Work sheet - http://www.cse4k12.org/binary/magic_trick.html
Magic Binary Cards - http://www.northeastern.edu/seigen/11Magic/Binary/Magic_binary_cards.pdf
Base 5 Number System – Basics - https://www.youtube.com/watch?v=qGi29E9q_f0
Binary Number System - https://www.mathsisfun.com/binary-number-system.html
Bits, bytes and words - http://www.plainenglish.info/Computer+Science/Computer+Architecture/Bits%2C+bytes+and+words